## Slide 1
Smart Grid Demonstration in City Subdivision of Panipat
17th August, 2016
Fuji Electric Co., Ltd.

## Slide 2: Challenge of India Power Distribution Companies
[Challenge] 1. Outage Management 2. Peak Load Management 3. Smart Meters 4. Capacity Building

## Slide 3: Improvement of KPIs
Improvement of reliability SAIFI/SAIDI by Multi-divided-Multi-connected network – Knowledge from TEPCO
Reduction in Distribution Transformer Failure Rate through TEPCO Technical Knowhow
AT&C Loss Reduction using Smart Meters
SAIFI : System Average Interruption Frequency Index SAIDI : System Average Interruption Duration Index

## Slide 4: Smart Grid Project Overview
Target country and areas : Republic of India, Haryana State, Panipat City
Distribution company : UHBVN (Uttar Haryana Bijli Vitran Nigam)
Demonstration period : September 2015 - March 2019
Demonstration scale (expense) : JPY 2,196 million (Including TAX)
Demonstration scale (target device) : 4 feeders, 11,000 smart meters
Project scope : Peak Load Reduction, Distribution System Monitoring and Control, Power Distribution Loss Reduction

## Slide 5: Panipat City, Haryana State
Panipat
Chandigarh
New Delhi
UHBVN (Uttar Haryana Bijli Vitran Nigam)
100km

## Slide 6: Smart Grids Feeder Management
Feeder_1
Feeder_2
Feeder_3
Feeder_4
: GO switch
Current Feeder Network
: New switch
: New HT Feeder
Feeder_1
Feeder_2
Feeder_3
Feeder_4
Multi divided and multi connected distribution network

## Slide 7: Feeder Structure
13-17
Mini
Secretariat
Panipat
Tehsil
Conduit
Salarganj
City-1
G T Road
Shree Ram
Sabji Mandi
Skylark
Vishwa Karma
Noorwala
Devi Mandi

## Slide 8: Smart Grid System Facilities
New Delhi
Hisar Data Center
Chandigarh
Haryana Power Training Institute (HPTI: Panchkula)
Demonstration Room
Training Room
Switchgear
Substation Panel
Smart Meter
Haryana Power Training Institute (HPTI)
Panipat Operation Center

## Slide 9: HPTI Demonstration Room
24.75ft = 7.54m
11.6ft = 3.54m
39.9ft = 12.16m
76.25ft = 23.24m
24.3ft = 7.40m
System Equipment Room
Indoor Equipment Room
Server Room

## Slide 10: TEPCO Training Center
VCB Panels / LBS / Smart Meters for Capacity Building
Power Control Panel
Single Line Diagram

## Slide 11: Indoor Equipment Room Layout

## Slide 12: LBS on Double Pole for Training

## Slide 13: 11,000 Smart Meters
RF Mesh Smart Meters
  4,900 : Single Phase Smart Meter
  600 : Three Phase Smart Meter
  RF Mesh : Primary Communication Platform
  GPRS : Secondary Communication Platform (for Backup)
TWACS Smart Meters
  4,900 : Single Phase Smart Meter
  600 : Three Phase Smart Meter
  TWACS : Supplementary Communication Platform
  RF Mesh : Primary Communication Platform
  GPRS : Secondary Communication Platform (for Backup)
  DCU : Requires additional 5,500 RF Mesh

## Slide 14: Smart Meter – RF Mesh & DCU
Data Concentrator Unit (DCU) for RF Mesh
Waiting for BIS Final Approval on September 2016

## Slide 15: Smart Meter 3 Communication Board
GPRS
RF Mesh
TWACS

## Slide 16
Server Equipment
Power plant
VCB Panel
Substation
LBS
(Load Breaking Switch)
LBS
SM
SM
SM
SM
Smart
Meter
SM
SM
SM
SM
SM
SM
SM
Radio Communication/GPRS(2G/3G)/TWACS(PLC)
SCADA
Billing System
(UHBVN)
OMS/ PLM
System Integration
System Structure
Head End System
MDMS

## Slide 17: Fuji Electric Smart Community Project in INDIA
Smart Grid in Panipat, Haryana State
New Smart City,
Maharashtra State
New Smart Capital, Andhra Pradesh State